## Slide 1
DUNCS — DoA Simulation Flow
Deep-Unfolded Sparse-Covariance ADMM for direction-of-arrival recovery
End-to-end walkthrough: config → system model → samples → model → subspace → RMSPE

## Slide 2
What is DUNCS?
Deep-Unfolded Sparse-Covariance ADMM — a learned algorithm for DoA estimation from sparse arrays.
The problem
• Estimate angles of M radio sources from
• N antenna snapshots over T time samples.
• Sparse arrays (MRA) save hardware but break
• classical subspace methods designed for ULA.
• Low SNR / few snapshots → the sample
• covariance R̂ₓ becomes noisy & non-Toeplitz.
The DUNCS idea
• Reconstruct a clean Hermitian-Toeplitz-PSD
• covariance R on the virtual co-array.
• Solve the convex reconstruction with ADMM,
• but unroll K iterations as a network.
• Make ADMM penalty/step parameters
• (ρ, τ, μ) per-iteration learnable.
• Feed the reconstructed R into a classical
• subspace method (ESPRIT / MUSIC).
• Train end-to-end on RMSPE between predicted
• and true DoA — a differentiable pipeline.
Why this presentation
• Trace one full DoA-simulation pass through
• the DUNCS code base, slide by slide.
• From YAML config to the final RMSPE number.
• Pointers to the exact files / classes that
• implement each stage.
• Companion to README.md and CLAUDE.md.
•
• Audience: anyone (or any Claude session)
• spinning up on the DUNCS code base.

## Slide 3
End-to-End Pipeline
main.py → SimulationRunner.run() — every box is a real class/function.
YAML config
load_simulation_config()
SystemModel
src/system_model.py
Samples (signals)
src/signal_creation.py
Dataset
src/data_handler.py
Model (DUNCS)
models_pack/sparse_cov_admm_unfold.py
Subspace (ESPRIT)
methods_pack/esprit.py
Loss / Eval (RMSPE)
metrics/criterions.py
Data path (per epoch)
• 1. Samples.samples_creation() draws random DoAs (gap-respecting)
• and synthesises the steering matrix A(θ).
• 2. x[t] = A(θ) s[t] + n[t] for t = 1..T snapshots.
• 3. R̂ₓ = (1/T) Σₜ x[t] x[t]ᴴ (sample covariance)
• 4. DataLoader batches (B,N,T) tensors with collate_fn.
• 5. Model receives x → returns predicted DoAs (θ̂).
Loss path (per batch)
• 1. DUNCS forward → reconstructed R̂ of size |U|×|U|.
• 2. ESPRIT(R̂, M) → estimated angles θ̂.
• 3. RMSPELoss(θ̂, θ) with permutation-invariant
• matching of the M sources.
• 4. backward() through every ADMM iteration: ρ, τ,
• μ are nn.Parameter tensors of length K.
• 5. AdamW + ReduceLROnPlateau schedule the learning rate.

## Slide 4
System Model — Array Geometry & Signal
src/system_model.py defines the physical array and the steering manifold.
Array geometry
• ULA — uniform linear array, N sensors at λ/2 spacing.
• MRA-N — minimum-redundancy array: N physical sensors,
• virtual ULA of size |U| via the difference co-array.
• Sparse arrays use sparse_array.py to compute U (virtual
• sensor indices) and the selection operator Φ.
• Optional perturbations: eta (position jitter),
• bias (uniform offset), sv_noise_var.
Signal model
• M sources at angles θ = (θ₁..θₘ), coherent or non-coherent.
• Far-field plane wave → steering vector a(θ) ∈ ℂ^N.
• Stack into steering matrix A(θ) = [a(θ₁)..a(θ_M)].
• Snapshots: x[t] = A(θ) s[t] + n[t], t = 1..T.
• s[t]: source amplitudes, n[t]: complex AWGN at given SNR.
• Output observation tensor: (B, N, T) complex64.
x[t] = A(θ) · s[t] + n[t] → R̂ₓ = (1/T) Σₜ x[t] x[t]ᴴ ∈ ℂ^{N×N}
Defaults from src/config/DUNCS.yaml
• N = 5 sensors M = 1 source T = 8 snapshots SNR = 30 dB
• array_form = 'ula' field_type = 'Far' signal_nature = 'non-coherent'
• doa_range = [−70°, 70°] min_gap = 5° between DoAs at training time

## Slide 5
Signal & Sample Generation
src/signal_creation.py — Samples class produces every training/test observation.
Samples.samples_creation() — per-sample recipe
• 1. Sample M DoAs:
• • set_doa() draws angles in [−70°, +70°]
• • enforces ≥ 5° gap (create_doa_with_gap)
• • picks a random extra offset per source
•
• 2. Build steering matrix:
• • SteeringVectorGenerator (singleton)
• • cached per (array geometry, frequency)
• • supports optional .mat antenna pattern
•
• 3. Synthesise snapshots x[t]:
• • source signals s[t]: complex Gaussian
• • noise n[t]: scaled by SNR
• • coherent mode → shared s across sources
•
• 4. Return tuple (x, θ, range, ...) into Dataset.
Dataset → DataLoader
• create_dataset(samples, N_samples, save?, paths, ...)
• • builds train and test splits separately
• • train_test_ratio = 0.1 by default
•
• Sample sizes (DUNCS.yaml defaults):
• • samples_size = 7000 training samples
• • 700 test samples
• • batch_size = 128
•
• collate_fn batches variable-length tensors;
• SameLengthBatchSampler groups same-T samples.
•
• dataset.materialize(system_model) re-computes
• derived quantities (R̂ₓ, masks) at the moment
• of use, instead of caching them on disk.

## Slide 6
DUNCS Forward Pass — Overview
src/models_pack/sparse_cov_admm_unfold.py — DUNCS.forward()
Sample covariance
R̂ₓ = (1/T) X Xᴴ
Measured projection
M = Φᴴ R̂ₓ Φ
Unrolled ADMM (K iter.)
R → S → T + duals
Subspace + DoA estimate
ESPRIT / MUSIC
What gets learned
• Per-iteration ADMM step / penalty parameters become nn.Parameter:
• • rho_r[k], rho_m[k] — R-update inversion coefficients (|U|² each, K iters)
• • tau[k] — soft-threshold for the SVT step (|U|-vector, K iters)
• • mu_u[k], mu_v[k] — dual ascent step sizes (scalars, K iters)
• The selection matrix Φ (built once from the array geometry) is frozen.
• Subspace method (ESPRIT) is parameter-free — it just does eigen-decomp.

## Slide 7
Step 1 — Measured Projection onto the Co-Array
Lift the noisy N×N sample covariance onto the |U|×|U| virtual co-array.
R̂ₓ = (1/T) X Xᴴ ∈ ℂ^{N×N} ➜ M = Φᴴ R̂ₓ Φ ∈ ℂ^{|U|×|U|}
What Φ is
• Φ (built by build_phi() from the sparse-array
• geometry) maps physical sensor indices
• to virtual co-array indices.
• Sparse layouts (e.g. MRA-5) yield |U| > N —
• a virtual ULA larger than the physical array.
• P = Φᴴ Φ (diagonal mask used in the R-update)
• is precomputed once and reused across all iters.
What we want to recover
• An |U|×|U| matrix R that is simultaneously:
• • Hermitian (R = Rᴴ)
• • Toeplitz (depends only on i−j)
• • PSD (R ⪰ 0)
• • Consistent with the measurements:
• Φᴴ R Φ ≈ M
• Subspace methods (ESPRIT) assume exactly
• this structure — they fail on R̂ₓ directly.
• DUNCS “denoises” into this feasible set.

## Slide 8
Step 2 — Unrolled ADMM (K iterations)
Each k = 1..K block runs five updates. K is fixed (default 20). Every ρ, τ, μ is learnable.
R-update
• Diagonal solve
• vec(R) = (P + 2ρ₝)⁻¹ · (vec(M) + ρ₝(S−U + T−V))
S-update (SVT)
• Singular Value
• Thresholding
• S = SVT_τ₊(R + U)
T-update
• PSD ∘ Toeplitz ∘ Herm
• T = Π_PSD(Π_Toep(Π_Herm(R+V)))
U dual
• U ← U + μ_u (R − S)
V dual
• V ← V + μ_v (R − T)
Why unroll instead of solving the convex problem to convergence?
• Fixed compute budget — K iterations → deterministic runtime, easy to deploy.
• Learned hyperparameters — ρ, τ, μ adapt to the SNR / snapshot regime.
• End-to-end gradient — the loss is on DoA, not on ADMM objective → the network
• can sacrifice optimisation purity for better downstream estimation.
• Test-time control — evaluate at K=20 (matched) or K=500 (classical ADMM)
• to confirm the learned net beats the converged baseline.

## Slide 9
Step 3 — Subspace Method + RMSPE Loss
After K iterations, the reconstructed T is fed to a parameter-free subspace estimator.
Subspace step — ESPRIT (default)
• Eigen-decompose T → signal subspace U_s of size |U|×M.
• Split U_s into two overlapping sub-arrays U₁, U₂.
• Solve U₁ Ψ = U₂; eigenvalues of Ψ → angles θ̂.
• Alternatives: music.py, root_music.py — same interface.
RMSPE — Root Mean-Squared Phase Error
• Pairs each predicted θ̂ with the closest true θ via
• permutation-invariant Hungarian matching.
• Wraps the residual to [−π, π) before squaring —
• avoids spurious 2π penalties.
• Differentiable wrt the subspace inputs → gradient
• flows back through ADMM into ρ, τ, μ.
L_RMSPE = √( (1/M) Σᵢ wrap(θ̂_π(i) − θ_i)² ) with π = arg min over permutations
Alternative criterion: ADMM objective
• Set criterion='admm_objective' to train on the ADMM
• residual itself rather than RMSPE — stable on hard regimes
• where supervised DoA matching is ambiguous (e.g. coherent sources).

## Slide 10
Training Loop
src/training.py — train() consumes the TrainingParams builder.
Per-epoch loop
• for epoch in 1..E:
• for batch (x, θ) in DataLoader:
• θ̂ = model(x, M, phase='train')
• loss = RMSPELoss(θ̂, θ)
• loss.backward()
• optimizer.step()
• validate on held-out split
• scheduler.step(val_loss)
•
• Saving:
• • final state_dict → data/weights/final_models/
• • per-config filename built by
• model.get_model_file_name()
Defaults (DUNCS.yaml)
• Optimizer AdamW
• Learning rate 5e-4 weight decay 1e-5
• Scheduler ReduceLROnPlateau
• step_size=40 gamma=0.5
• Epochs 90
• Batch size 128
• samples_size 7000 (train) + 700 (test)
• Training objective 'angle'
•
• All five ADMM parameter vectors are jointly
• optimised end-to-end with the rest of the model;
• ESPRIT contributes only via the chain rule on θ̂.

## Slide 11
Evaluation — Baselines and CRB
src/evaluation.py — evaluate() compares the learned model against fair baselines.
What gets scored
• Trained DUNCS @ K=20 —
• the headline number.
• Trained DUNCS @ K=500 —
• sanity check that learned
• rates still beat plain ADMM.
• Classical ADMM @ K=20, 500
• on the same sample covariance.
• Plain sample-covariance ESPRIT —
• no reconstruction at all.
• Other models (SubspaceNet,
• DA-MUSIC, TransMUSIC, ...)
• if enabled in evaluation.models.
Metric: test RMSPE
• Reported per (model, K, scenario).
• Averaged over Monte-Carlo runs
• if monte_carlo_simulations > 1.
• Scenario sweeps in YAML let you
• plot RMSPE vs SNR or T
• with a single config run.
• Outputs:
• • score logs in data/simulations/
• /results/scores/
• • plots in .../results/plots/
The CRB floor
• src/metrics/crb.py computes the
• Cramér–Rao Bound on the DoA
• variance for the current
• (N, M, T, SNR) configuration.
• Drawn as a dashed line on every
• RMSPE-vs-X sweep.
• Any model below CRB is a bug;
• a model close to CRB is
• statistically efficient.

## Slide 12
How to Run / File Map
Quick reference for landing in the code base.
Commands
• pip install -r requirements.txt (Python 3.10+, PyTorch 2.6)
•
• python main.py duncs # single DUNCS sim
• python main.py sparsenet # SparseNet baseline
• python compare_models.py # DUNCS vs SparseNet, shared dataset
• python train_single_model.py # standalone trainer
•
• Output goes under data/:
• • data/datasets/ — cached if save_dataset: true
• • data/weights/ — model state_dicts
• • data/simulations/results/ — score logs + plots
Key files for the DoA flow
• main.py — entry, picks YAML config
• run_simulation.py — SimulationRunner.run()
• src/config/DUNCS.yaml — all hyperparameters
• src/config/simulation_config.py — OmegaConf dataclasses
• src/system_model.py — array, steering vectors
• src/signal_creation.py — Samples (generates x[t])
• src/data_handler.py — Dataset + DataLoader
• src/models_pack/sparse_cov_admm_unfold.py — the DUNCS model
• src/methods_pack/esprit.py — subspace estimator
• src/metrics/criterions.py — RMSPELoss
• src/metrics/crb.py — Cramér–Rao Bound
• src/training.py — train() loop
• src/evaluation.py — evaluate() loop